## Slide 1: Model Design
Treasure Valley Groundwater Flow Model Training
Stephen Hundt, USGS (shundt@usgs.gov)
March 14th, 2023

## Slide 2: Contents
Model basics
Non-irrigation boundaries and stresses
Irrigation boundaries and stresses

## Slide 3: Model basics

## Slide 4: Study area

## Slide 5: Grid
64 x 65 1 mile square grid
Regional model, 1 mile cell, doesn’t have all local heterogeneity, not designed for impacts of individual pumping wells or the impact at individual observation wells

## Slide 6: Layers
6 layers – chosen mostly from observed vertical head gradients
Incorporates info from hydrogeologic framework
Several pinch in the west

## Slide 7: Time
360 monthly periods
1986-2016
Most stress data is precise to 1 month or larger periods
Not all data available during the whole period
Change over the period

## Slide 8: Observation targets
Water level and flux targets and derivatives thereof

## Slide 9: Non-irrigation boundaries and stresses

## Slide 10: Tributary underflow
Based upon precipitation in tributary watersheds
Enters at cells on boundary

## Slide 11: Lake Lowell
General head boundary
Covers multiple cells
Surface area varies with time – multipliers applied to adjust when lake doesn’t fully cover model cell
Stage varies with time

## Slide 12: Rivers
River package
Stage varies with time in Boise and Payette
Divided into reaches with equal properties and between gaging locations

## Slide 13: Drains
Drain boundary
“Catchment” areas of major drains mapped
Drain catchment areas have equal conductance
Major source of discharge
Good control on these with drain discharge observations

## Slide 14: Irrigation boundaries and stresses

## Slide 15: Canal leakage: New York Canal
Upper
Well package
Leakage set as percentage of diversion in canal
Multipliers applied to cells in proportion to length of canal within cell
Lower
River package
Areas of high water table

## Slide 16: Canal leakage: Other
Well
Set as proportion of diversion to an irrigation entity
Only information is diversion to irrigation entity, location of fields, and location of canals
(modified from Faunt, 2009)

## Slide 17: Incidental recharge
Well package
Estimated
Agricultural and (sub)urban have different properties
(modified from Faunt, 2009)

## Slide 18: Pumping
Well package
Measurements were available for some municipal and industrial
Other (most) pumping is estimated
Pumping from multi-layer synthetic wells is distributed in proportion to K * open length

## Slide 19: Data sources
Didn’t have direct estimates for these stresses (except some pumping)
Irrigation entity area
Diversions
Irrigation status
Evapotranspiration
Precipitation
Canal locations
Groundwater water rights
Well construction

## Slide 20: Irrigation entities
Locations of irrigation entities from state
A few smaller ones were combined
Deliveries from diversions are only known at this scale

## Slide 21: Diversions
sdf
Locations on the river
Monthly volumes
Irrigation entity (destination)

## Slide 22: Irrigation status
Eight years were meticulously digitized
Irrigated, semi-irrigated, non-irrigated
Used to set irrigation related fluxes and properties

## Slide 23: Evapotranspiration
sdf
Monthly evapotranspiration rasters with a resolution of 30 meters
Provides valuable information on consumptive use – spatial and temporal patters
Made up of combination of methods, include 8 years of METRIC

## Slide 24: Precipitation
sdf
PRISM
Monthly

## Slide 25: Canal locations
Broad categories
  Major, minor, feeder, etc
No properties known other than location
  Width, depth, conductance

## Slide 26: GW rights
Point of diversion record provides location, type, and right
Used to estimate cells in which estimated pumping occurs

## Slide 27: Well construction
Irrigation wells
Subset of well logs of each type were retrieved
Open intervals were recorded
Synthetic wells were placed, using a weighted average of open length in different layers
Domestic wells

## Slide 28: Approach
Calculations
Parameters
Demand and supply utility

## Slide 29: Approach

## Slide 30: Spatial Scale
Inputs are at multiple scales
Leakage, pumping, irrigation infiltration are calculated at irrigation entity scale
Stresses then distributed to cells
Distribute using finer-scale information
  ET
  Irrigated lands
  Canal location
  Well water rights

## Slide 31: Spatial distribution
Infiltration: ET and irrigation status

## Slide 32: Spatial distribution
Canal leakage
Proportional to irrigated area
AND
Proportional to major canals
Estimated tradeoff

## Slide 33: Spatial distribution
Unmeasured pumping
Proportional to GW right